## Slide 1: SMART INDIA HACKATHON 2026
Problem Statement ID – SIH26123
Problem Statement Title- Edge-AI Based Distributed Fleet Coordination for Autonomous Mobile Robots (AMRs) in Smart Warehouses
Theme- Smart Automation
PS Category- Software
Team ID- 147189
Team Name- CLUSTER HEAD

## Slide 2
CLUSTER HEAD
Problem at Hand
Centralized Dependency: Movement coordination can depend on a central controller and communication path.
Traffic Conflicts: Multiple AMRs competing for narrow aisles and junctions can cause blocking and collisions.
Deadlock & Starvation: Fixed-priority rules can repeatedly make the same robot yield, causing prolonged waiting and unfair access to shared lanes.
Dynamic Warehouse: Blocked aisles or changing routes require robots to adapt their paths instead of following a fixed route.
Our Solution
Why We Stand Out
Scalability Challenge: As the number of AMRs increases, coordinating every movement through one controller can increase the coordination burden and communication dependency.
Distributed Decisions: Each AMR performs its own path planning and conflict decisions. The dashboard only monitors; it does not control robot movement.
Fairness-Aware Priority: Waiting time increases a robot's priority, reducing repeated starvation during recurring conflicts.
Pre-emptive Coordination: Robots negotiate before entering a contested narrow lane, instead of reacting after a conflict occurs .
Dynamic Re-planning: When an aisle or grid cell becomes blocked, the affected robot can re-run A* and find an alternative route.
Design Philosophy
Local First — Each AMR owns its movement decision.
Predict Before Conflict — Negotiate before entering shared space.
Fairness by Waiting — Waiting increases future priority.
Deterministic Decisions — Priority score + robot-ID tie-breaker.
Monitor, Don't Control — Dashboard observes; robots decide.
Cell-Level Deadlock Resolution: If a physical block persists, the lower-priority robot moves to an available backup cell and replans.

## Slide 3: TECHNICAL APPROACH
CLUSTER HEAD

## Slide 4: FEASIBILITY AND VIABILITY
CLUSTER HEAD
ANALYSIS OF THE FEASIBILITY
Dimension | Assessment
Technical | Proven methods: A* path planning + rule-based scoring No model training or specialised hardware required
Proof of concept | Working 3-robot prototype in Python + Pygame
Operational | Decentralised: each robot makes its own decisions Dashboard is monitor-only; it never controls robots
Safety and reliability | Robots negotiate right-of-way before a narrow lane Score = 0.5(priority) + 0.3(urgency) + 0.2(wait factor); Ties – Lower Robot ID
Scalability | Identical logic per robot; fleet size can be extended Path: Simulation -- Edge hardware (Pi / Jetson)
Cost and resources | Open-source stack; No cloud or license costs Runs on a standard laptop
Measurability | Logs collisions, waiting time, messages, completion time Target: ≥20% reduction in total task completion time vs stop-and-wait baseline
POTENTIAL CHALLENGES AND WAYS TO OVERCOME THEM
Challenges / Risks | Mitigation
Unfair priority decisions | Adjust priority settings Test across settings; Every run should be logged Priority based on Urgency+Waiting time
Stale or lost messages | Timestamped messages published every 1 s Robots use the latest valid peer state before entering a contested lane
Inconsistent robot decisions | Identical scoring formula and message format Deterministic tie-break using robot ID
Starvation and deadlock | Waiting time increases Priority score, helping reduce starvation Deterministic tie-breaking provides predictable conflict resolution.
Limited local view | Robots broadcast Position,Target,Priority,Urgency,Wait time and ETA every 1s
Scaling beyond 3 robots | Compact, fixed-size messages Test 4–5 robots once the core is stable
Simulation-to-real gap | Agent code is independent of hardware Pi / Jetson trial planned for next phase
Scope: 3 AMRs with decentralized coordination, A* planning, Conflict resolution, Dynamic rerouting and Task reassignment is proposed as an extension
Future: Edge deployment, Real-world validation and larger fleets.

## Slide 5
IMPACT AND BENEFITS
0
collisions observed in tested simulation runs
Target ≥ 20%
Reduction in Task Completion Time (vs. Stop-and-Wait)
1 s
P2P State & Intent Broadcast Frequency
Local
Decision Making
(No Central Movement Controller)
IMPACTS (Who It Helps)
Warehouse Operators & Fleet Managers
•
Reduced Central Dependency: robots can continue local coordination when the control-room connection is unavailable.
Real-Time Fleet Oversight : Read-only visual dashboard provides complete live status, battery levels, and telemetry without controlling or delaying robot paths.
Warehouse Floor & Safety Supervisors
•
Pre-emptive Conflict Resolution: robots negotiate right-of-way before entering contested narrow aisles, reducing collision risk.
•
Deadlock/Starvation Handling: wait-time escalation and deterministic tie-breaking help robots progress through repeated bottleneck conflicts.
Logistics & Supply Chain Operations
•
Adaptive Obstacle Detours : Robots locally recalculate alternative routes around blocked aisles using A*, minimizing delivery downtime.
•
Fair Resource Sharing : Dynamic wait-time priority scaling helps reduce repeated blocking and starvation.
IT & Edge Deployment Engineers
•
Lightweight Hardware Footprint : Designed for lightweight edge deployment (e.g., Raspberry Pi / Jetson) without requiring complex middleware.
•
Low Network Strain : Replaces continuous heavy cloud streaming with lightweight, periodic peer-to-peer JSON messages.
Maximized Productivity
Targets ≥20% faster task completion compared to traditional stop-and-wait approaches.
Reduced Single Point of Failure
Removes central server dependency by embedding local pathfinding (A^*) and priority logic directly onto each robot.
Pre-Emptive Conflict Resolution
AMRs negotiate narrow-lane access prior to entry rather than reacting after proximity warnings.
Anti-Starvation Fairness
Priority Score (α·P + β·U + γ·W) automatically escalates for waiting robots,helping reso lve repeated bottleneck conflicts.
Deterministic Tie-Breaking
Resolves equal priority scores predictably using unique Robot IDs to ensure reproducible fleet execution.
Simulated & Tested
Multi-agent 2D Python/Pygame testbed with 3 AMRs; 0 collisions observed across tested scenarios.
Full Telemetry Transparency
Dedicated Pygame dashboard logs positions, status, battery, and P2P chatter for complete auditability.
Autonomous Battery Management
Robots monitor battery level, route to charging stations when critically low, charge, and resume their saved task.
Lightweight P2P Communication
Robots exchange compact state messages every 1 sec , reducing dependence on continuous centralized communication.
5
CLUSTER HEAD
•

## Slide 6: RESEARCH AND REFERENCES
CLUSTER HEAD
REFERENCES
Problem Statement: SIH26123, "Edge-AI Based Distributed Fleet Coordination for Autonomous Mobile Robots (AMRs) in Smart Warehouses," Bharat Electronics Limited (BEL), Smart India Hackathon 2026.
VDA 5050 Standard: VDA 5050 v3.0.0, "VDA Specification for AGV Communication Interface," Verband der Automobilindustrie (VDA), 2023.
Open-RMF Traffic Negotiation: Open Robotics, "Open-RMF Traffic Management and Negotiation Library (rmf_traffic)," Open Source Robotics Foundation, 2023.
Lifelong MAPF Research: J. Li et al., "Lifelong Multi-Agent Path Finding in Large-Scale Warehouses," Proceedings of the AAAI Conference on Artificial Intelligence, Vol. 35, No. 13, pp. 11272–11281, 2021.
A Pathfinding Basis: P. E. Hart, N. J. Nilsson, and B. Raphael, "A Formal Basis for the Heuristic Determination of Minimum Cost Paths," IEEE Transactions on Systems Science and Cybernetics, Vol. 4, No. 2, pp. 100–107, 1968.
What research establishes: Key findings from literature
Local A* Pathfinding: A*: Established grid-based path-planning algorithm suitable for local route calculation. Peer-to-Peer Communication Protocols: Established mechanism for direct inter-agent state and intent exchange without central brokers.
Lifelong MAPF Foundations: Establishes theoretical multi-agent pathfinding and spatial access reservation in shared warehouse environments.
Standardized Fleet Interfaces (VDA 5050 / Open-RMF): Demonstrates standardized data structures for mobile robot coordination and traffic management.
What existing systems do: Evidence from current solution
Centralized Fleet Controllers: Provide global fleet tracking but create single points of failure and high network latency.
VDA 5050 Standard Interface: Standardizes central control-to-AGV communication, but does not offer direct robot-to-robot P2P negotiation.
Open-RMF Traffic Negotiation:. Provides multi-robot traffic scheduling and negotiation; our prototype focuses on lightweight local decision-making. Fixed-Priority Decentralized P2P: Uses local P2P with static rules (e.g., fixed Robot ID), Static priority rules can repeatedly favor the same robot, increasing starvation risk.
RESEARCH GAP : What is still missing
Over-reliance on Central Control: Centralized architectures depend on network connectivity and fleet-control availability.
Absence of Anti-Starvation Priority: Static scoring frameworks lack dynamic wait-time escalation, causing corridor deadlocks.
Reactive vs. Pre-emptive Avoidance: Systems rely on reactive stop-and-wait sensors rather than pre-entry narrow-lane negotiation.
Heavy Compute Burden: More advanced MAPF approaches can introduce additional computational and coordination complexity; our prototype focuses on lightweight local planning.